## Slide 1: Estimation of demolition and new construction of housing in US counties until 2060 Implications for building material reuse potential
Peter Berrill
ICWMT 15, June 30, 2020
Notes: While many of the lectures in this course will deal with the nuts and bolts of how buildings work and how they use energy, this talk presents a top down analysis of recent trends and drivers of US REC.

## Slide 2: Dynamic Stock Models of Buildings
Müller, D.B (2006), Ecol. Econ., ‘Stock dynamics for forecasting material flows—Case study for housing in The Netherlands’
Drivers (Inputs)
Dynamic Stock Model
Results, over time
Inputs (construction)
Outputs (demolition)
Total Stock
Notes: Valuable not only in terms of economic worth, but crucial to everyday life. We pay a lot of money for housing. More than anything else.
If we pay so much for housing, it is one of the major ways we can affect our footprints through what we buy.
We should also aim to be comfortable and healthy in our homes. Something that requires energy, but the amount of energy required to maintain healthy comfortable conditions varies a lot by home type (and climate).

## Slide 3: Dynamic Stock Models of Buildings
Lanau et al. (2019), Env. Sci. Tech., ‘Taking Stock of Built Environment Stock Studies: Progress and Prospects’, Fig. 2
b) Tag cloud of the journal article authors
c) Network of coauthorship
Notes: Valuable not only in terms of economic worth, but crucial to everyday life. We pay a lot of money for housing. More than anything else.
If we pay so much for housing, it is one of the major ways we can affect our footprints through what we buy.
We should also aim to be comfortable and healthy in our homes. Something that requires energy, but the amount of energy required to maintain healthy comfortable conditions varies a lot by home type (and climate).

## Slide 4: Current research goals
Identify strategies for GHG reduction from US residential buildings, all life cycle stages
Model and project results of
  Energy demand
  Construction material requirements and waste generation
  Comprehensive GHG emissions from residential sector activities
Data needs: housing stock by type, age, location

## Slide 5: US residential sector in context global GHG emission
In top 2 emitters of residential GHG emissions globally: ~1Gt CO2 from energy, 0.2Gt CO2 from construction. Reducing by ~1.5% annually, due to low-C electricity

## Slide 6: US housing mostly older & single-family
EIA, 2018
Own calculations, based on several sources

## Slide 7: Spatially disaggregated housing stock – Single-family

## Slide 8: Spatially disaggregated housing stock – Multifamily

## Slide 9: Spatially disaggregated housing stock – Manuf. Homes

## Slide 10: Single-family and Multifamily homes, NY State

## Slide 11: Basic stock model equations
Ct+1 = (St+1 - St) + Dt+1
C = new construction, D = demolition, S = stock = V*O
V = vacancy ratio = total units/occupied units; O = occupied units
New construction can results from St+1 > St, from Dt+1 > 0, or from Vt+1 > Vt
Notes: Need to change the formulation to allow for varying vacancy rates. So that counties with shrinking populations can have increasing vacancy rates, and counties with rapidly increasing population could have smaller vacancy rates, at least for a while.
Also need to allow for changes in the type splits. Currently the type split is kept constant across counties.

## Slide 12: Projections of demolition, based on lifetime distribution
Year of construction (<1890 to 2017) based on decadal Censes, various survey data, and estimates by Moura et al (2015)
Lifetime distribution functions estimated per each decadal cohort (1940s, 1950s, etc.)

## Slide 13: What is the lifetime of a house in the US?
Sources: Keolian et al (2001); Aktas & Bilec (2012); Moura et al (2015); Ianchenko et al (2020)

## Slide 14: What is the lifetime of a house in the US?
Sources: Keolian et al (2001); Aktas & Bilec (2012); Moura et al (2015); Ianchenko et al (2020). See also Miatto et al (2017)
Median lifetimes estimated based on Weibull lifetime distribution functions for different vintages

## Slide 15: Method to project future demand for housing
Ct+1 = (St+1 - St) + Dt+1
Estimate future stock of total housing per county based on three factors:
  Population by house type
  Household size by house type
  Vacancy rate by house type

## Slide 16: 1. Q: Who would estimate future population at local scale?
A: Hauer (2019) scaled SSP population projections to 2100 to US county level

## Slide 17: 1. Q: Who would estimate future population at local scale?
A: Hauer (2019) scaled SSP population projections to 2100 to US county level

## Slide 18: 1. Implementation of Hauer Population Data
Scaled SSP2 to match the main series from the USCB population projection
Assumed no change in house type split of population per county, for now

## Slide 19: 2. Projections of household size
Like most countries, US has seen notable decline in household size
I use data from McCue (2018) to project further modest reductions from 2020-2060, with the same average reduction applying evenly to different house types and counties
Moura et al (2015)

## Slide 20: 3. Occupancy/vacancy rates by county
10% of SF homes are vacant. 15% for MF, 22% for MH. Lowest rates since mid-1980s

## Slide 21: 3. How will vacancy rates develop?
On downward trend, construction is currently not keeping up with population growth, & large increase in demand for rental housing

## Slide 22: How will vacancy rates develop?
Currently no modeled change in vacancy rates. Adapt -> reduce vacancy in growing/highly regulated counties. Increase vacancy in declining counties
Housing construction highly restricted, vacancy rates may decline
Population decreasing, low demand for new housing, vacancy rates may increase
Glaeser & Gyourko (2018), Jour. Econ. Per., ‘The economic implications of housing supply’

## Slide 23: Results: National annual construction and demolition
National total

## Slide 24: Results: National annual construction and demolition
Maricopa Cty, AZ

## Slide 25: Results: National annual construction and demolition
Cochise Cty, AZ

## Slide 26: Results: National annual construction and demolition
New Haven Cty, CT

## Slide 27: Implications for material reuse
Circular economy potential may exist for bulk construction material in some counties
With further refining of our model and investigating of local effects, we can find out which locations have highest/lowest potential for material reuse
Currently only considering one sector – residential buildings. Broadening scope to include non-residential buildings, roads, and other infrastructure can give more insights

## Slide 28: Where does construction waste currently go?
Most end-of-life concrete currently goes back into road bases, only a small part goes back into new concrete
Townsend et al (2018), Waste Mgmt., ‘CDDPath: A method for quantifying the loss and recovery of construction and demolition debris in the US’

## Slide 29: Next steps
Assumptions regarding vacancy rates
Calculation of material intensity of housing, to estimate material flows
Investigate environmental benefit of circular material flows
Energy scenarios based on lifetime distribution, household size, housing type mix

## Slide 30: Thank you!
peter.berrill@yale.edu
https://github.com/peterberr
https://www.researchgate.net/profile/Peter_Berrill